## Slide 1: CPU microarchitectures (2000-2018)

## Slide 2: CPU Microarchitecture
Branch prediction
  conditions, indirect branches, call/return pairs
  speculative execution
Instruction decoder
  loop cache (simple loops up to ~20 instructions)
  conversion to micro-ops (1:1, 1:N, 2:1)
  stack-pointer simulator
Renamer
  16 architectural integer registers mapped to ~160 physical
    similarly for FP/vector registers
Out-of-order execution
  ~40 micro-ops in simultaneous execution (RS) from a window of ~300 (ROB)
  retirement: memory/register stores in-order in background
  store forwarding: loads retrieve values from waiting stores
  speculative loads: no waiting for waiting stores (to unknown addresses)

## Slide 3: Intel vs. AMD architectures (realworldtech.com)

## Slide 4: AMD Zen+ (2018) [wikichip.org]

## Slide 5: AMD Zen+ (2018) [wikichip.org]

## Slide 6: Intel Ice Lake (2019) [wikichip.org]

## Slide 7: Intel Ice Lake (2019) [wikichip.org]

## Slide 8: CPU Microarchitecture (Intel x86/64, 2015..2023)
In a cycle, CPU can (in theory) simultaneously perform:
  Fetch: 16 B (avg. 4 instructions) from L1 instruction cache
  Decode: 5..6 instructions
  ALU: 3..5 simple operations (add/mul)
  Memory load: 2..3 reads (up to 256..512 bits total) from L1 data cache
  Memory store: 1..2 writes (up to 256..512 bits total) to L1 data cache
Latency
    the time between consuming operands and producing results
  integer add: 1, mul: 4
  FP add: 2..4, FP mul/FMA: 4
  FP div: 11/14, integer div: ~18, data dependent
  integer load: 5, FP load: 6 (L1 cache)
  store address: 3
  store data: 1..2 (retirement, in-order)